## Slide 1
IoT • TINYML • EDGE AI
Energy-Efficient
TinyML-Based IoT System
for Real-Time Condition
Monitoring
ESP32 • Vibration + Temperature • On-device monitoring
PROJECT TEAM
P. Uday — 2520090089
A. Sri Chaitanya — 2520090094
Dharshan — 2520090088
Mrudula — 2520090073
SENSORS → ESP32
EDGE CLASSIFICATION
LEDs • OLED • BUZZER
Real-time condition monitoring

## Slide 2
Project Overview
Monitors vibration and environmental temperature/humidity.
ESP32 reads sensors and classifies the condition as Normal, Warning, or Abnormal.
OLED shows readings; LEDs and buzzer provide local alerts.
Designed for compact, low-cost, edge-based monitoring.

## Slide 3
Problem Statement & Objectives
Unexpected vibration or overheating can indicate equipment problems.
Provide continuous, near-real-time condition monitoring.
Give clear visual and audible alerts when limits are exceeded.
Reduce dependence on cloud processing by handling decisions on the ESP32.

## Slide 4
Hardware Components
ESP32 DevKit V1 — main controller.
MPU6050 — accelerometer/gyroscope for motion and vibration.
DHT22 — temperature and humidity sensor.
0.96-inch I²C OLED — displays readings and status.
Green / Blue / Red LEDs, buzzer, push button, resistors, breadboard, jumper wires.

## Slide 5
System Architecture
Sensor data is processed locally on the ESP32.
MPU6050 + DHT22
ESP32 Sampling
Threshold Decision
OLED + LEDs + Buzzer
→
→
→
Sampling interval: 500 ms
Classification in the supplied code uses vibration thresholds.

## Slide 6
Circuit Wiring Diagram
ESP32 connections to MPU6050, DHT22, OLED, indicators and button.

## Slide 7
Key Pin Connections
I²C bus: SDA GPIO 21, SCL GPIO 22 (MPU6050 and OLED).
DHT22 data: GPIO 4.
Green LED: GPIO 25; Blue LED: GPIO 26; Red LED: GPIO 27.
Buzzer: GPIO 18; push button: GPIO 19 using INPUT_PULLUP.
Check the physical wiring and sensor power requirements before powering the board.

## Slide 8
Software & Operating Logic
Develop and upload the sketch using Arduino IDE; test the circuit in Wokwi where supported.
Read MPU6050 acceleration and calculate vibration magnitude.
Read temperature and humidity from the DHT22.
Normal: vibration < 2.0 m/s²; Warning: 2.0–4.0 m/s²; Abnormal: ≥ 4.0 m/s².
Push button toggles audible alerts; OLED and Serial Monitor report readings.

## Slide 9
Code Snapshot — Setup & Sensors
Core excerpt from the supplied Arduino sketch.
Wire.begin(SDA_PIN, SCL_PIN); dht.begin(); if (!mpu.begin()) { Serial.println("ERROR: MPU6050 not detected!"); while (true) delay(1000); } float magnitude = sqrt(x*x + y*y + z*z); float vibration = fabs(magnitude - 9.81); float tempC = dht.readTemperature(); float humidity = dht.readHumidity();
Libraries required: Adafruit MPU6050, Adafruit Unified Sensor, Adafruit GFX, Adafruit SSD1306, DHT sensor library.

## Slide 10
Code Snapshot — Classification & Alerts
if (vibration < WARNING_LIMIT) { condition = 0; status = "NORMAL"; } else if (vibration < DANGER_LIMIT) { condition = 1; status = "WARNING"; } else { condition = 2; status = "ABNORMAL"; } if (condition == 0) digitalWrite(GREEN_LED, HIGH); else if (condition == 1) digitalWrite(BLUE_LED, HIGH); else { digitalWrite(RED_LED, HIGH); if (alertsEnabled) tone(BUZZER_PIN, 2000); }
This is threshold-based classification; it is not a trained TinyML neural network.

## Slide 11
Benefits, Limitations & Future Scope
Benefits: low-cost hardware, local response, visible/audible alerts, no cloud required for basic operation.
Limitations: threshold selection needs testing; DHT22 measures ambient conditions, not every machine's internal temperature.
The provided sketch does not implement a trained TinyML model or prove measured energy savings.
Future work: collect labelled data, train and deploy a small model, measure power use, and add logging/connectivity.

## Slide 12
Conclusion & Project Team
Energy-Efficient TinyML-Based IoT System for Real-Time Condition Monitoring
ESP32 combines sensor readings with on-device condition decisions.
OLED, LEDs and buzzer make system status easy to understand.
Next step: validate thresholds and evaluate a trained TinyML model.